SOP 4. Standard Operating Procedure for Pyrophoric Chemicals

I. 	General Statement of Coverage

Pyrophoric chemicals are chemicals that will ignite in air (below 130 °F) in the absence of 	added heat, shock., or friction. Common pyrophoric solids include Titanium Dichloride and 	Phosphorous. Sodium, Butyllithium, and Lithium Hydride are spontaneously flammable in 	moist air, as they react exothermically with water.

II.	Hazard Assessment

A Job Hazard Assessment should be performed for work involving corrosive materials and should address the issues of proper use and handling, chemical toxicity, storage, disposal, spill response, and required PPE.  See Section 21 and Form 4 of Section 25.0 of the Chemical Hygiene Plan.

III.	Resources

- Available Training

Chemistry 685

EHS/Chemistry Lab Safety Course

- Text and Literature References

Department of Chemistry Safety Handbook

- CHP Appendix III (Section 23.3) Chemical Information Tables

Table 5. Water Reactive Chemicals

Table 8. Peroxide Forming Chemicals

IV. 	Chemical Storage

A. 	Special Storage

1. Pyrophoric chemicals should be stored under an inert atmosphere or solvent as 			appropriate. Do not store pyrophoric chemicals with flammable materials or in a 			flammable-liquids safety cabinet. Store these materials away from sources of ignition. 		Minimize the quantities of pyrophoric chemicals stored in the laboratory.

2. Never return excess chemicals to the original container. Small amounts of impurities 		may be introduced into the container which may cause a fire or explosion.

B. 	Gas Cylinders

Gas cylinders must be secured while in use or in storage (empty or full). They should be 		stored with the valve cap secured. Refer to SOP #6-Compressed Gases.

V. 	Personal Protective and Emergency Equipment

A. 	Eye and Face Protection

Refer to the Eye Protection Policy, Appendix IIB (Section 23.2). At a 				minimum, safety glasses with permanently attached top and side shields must be worn 		in the laboratory. These glasses, however, do NOT protect against splash hazards. When 		performing a hazardous activity, a face shield must be worn in addition to the safety 		glasses OR switch to chemical splash goggles (with shielded ventilation ports). Face 		shields are available from the Safety Office (free of charge).

B. 	Gloves

Appropriate gloves should be worn when handling hazardous materials. The selection 		of glove materials should be made from Appendix II, Part A (Section 23.2) of the CHP. 		If this chart is insufficient, please see the Safety Coordinator/CHO.

C. 	Protective Clothing

Lab coats, closed toed shoes and long sleeved clothing should be worn when handling 		hazardous materials. Additional protective clothing, such as aprons or full-length arm 		protection, should be worn if the possibility of skin contact is likely.

D. 	Hearing Protection

The use of hearing protection requires monitoring and training. See the Safety 			Coordinator/CHO for details.

E. 	Respirators

The use of respirators require medical certification, fit testing, and training. See the 		Safety Coordinator/CHO for details.

F. 	Eye Wash

Where the eyes or body of any person may be exposed to hazardous materials, suitable 		facilities for quick drenching or flushing of the eyes and body shall be provided within, 		or near, the work area for immediate emergency use. Bottle type eyewash stations are 		not acceptable.

G. 	Safety Showers

A safety shower should be available and functioning as specified by ANSI Z358.1.

H. 	Fire Extinguishers

All laboratories must contain at least one Carbon Dioxide (Type B-C) or Dry Chemical 		(Type A-B-C) fire extinguisher. Additional fire extinguishers are located near exits 		and/or stairwells in each building. Special Class D fire extinguishers (for certain metal 		and pyrophoric material fires) are available from the Safety Office.

VI. 	Controls

A. 	Designated Areas

Some reactive materials such as Pentaborane require Designated Areas. See Section 18 		of the CHP.

B. 	Chemical Fume Hoods

Use pyrophorics in a chemical fume hood or glove box. With a fume hood, use portable 		safety shielding and work with the sash as far down as feasible (see below). Also, refer 		to the SOP on using glove boxes.

C. 	Glove Boxes

Refer to SOP 14 on the use of Dry Boxes.

D. 	Safety Shielding

Safety shielding is required any time there is a risk of explosion, splash hazard or a 		highly exothermic reaction. All manipulations of water sensitive and pyrophoric 			chemicals which pose this risk should occur in a fume hood with the sash in the lowest 		feasible position. Portable shields, which provide protection to all laboratory occupants, 		are acceptable.

E. 	Special Ventilation

Special ventilation is required if these materials are used outside of a fume hood. If your 		research does not permit the handing of pyrophoric chemicals in a fume hood, contact 		the Chemical Hygiene Officer or the Division of Environmental Health and Safety to 		review the adequacy of all special ventilation.

F. 	Vacuum Protection

1. Evacuated glassware can implode and eject flying glass, and splattered chemicals. 		Vacuum work involving flammable liquids must be conducted in a fume hood, glove 		box or isolated in an acceptable manner.

2. Mechanical vacuum pumps and the “House Vacuum System” must be protected 		using cold traps and, where appropriate, filtered to prevent particulate release. See the 		article in the Department Safety Handbook under “Compressed Gases.” The exhaust for 		the pumps must be vented into an exhaust hood or local exhaust system.

G. 	Signs and Labels

1. Doorways: All OSHA Select Carcinogens, Reproductive Toxins, Highly Toxic 			materials, and NFPA Level 4 Flammable Liquids (Appendix III, Tables 10-15) must be 		indicated on the acrylic door sign.

2. Containers: All hazardous materials must be clearly labeled with the correct chemical 		name.

H. 	Utilities

In Evans and Celeste Labs, utility shut-off valves are located in pipe chases just outside 		of the laboratories. In Newman/Wolfrom, the valves are located above the ceiling in the 		hallways. Look for the ceiling tiles with the green dots.

I. 	Fire Protection

Older buildings, such as Evans and Johnston Labs, do not have sprinkler suppression systems.  This could be a consideration for storing or using large quantities of hazardous materials.

VII. 	Specific Procedures

Refer to the MSDS or other sources of information to become familiar with the properties of 	the particular substances including: chemical and physical properties, health hazard 	information, symptoms of over-exposure, etc.

VIII. 	Emergency Procedures

A. 	Notification

Refer to the “Emergency Response” section of the Department Safety Handbook for 		generic emergency response procedures. Specific emergency procedures should be 		developed for each group or laboratory. The procedures should address as a minimum 		the following:

1. Who to contact: (University police at 292-2121 or 292-2525, and Division of 			Environmental Health and Safety at 292-1284 during normal working hours, and the 		Principal investigator of the laboratory including evening phone number).

2. The location of all safety equipment (showers, spill equipment, eye wash, fire

extinguishers, etc.).

3. The location and quantity of all water sensitive chemicals in the laboratory.

4. The method used to alert personnel in nearby areas of potential hazards

5. Special first aid treatment required by the type of pyrophoric chemicals handled in 		the laboratory.

B. 	Spill Response

1. Anticipate spills by having the appropriate clean up equipment on hand. The 			appropriate clean up supplies can be determined by consulting the material safety data 		sheet. This should occur prior to the use of any pyrophoric chemicals or water sensitive 		chemicals. Spill control materials for pyrophoric chemicals or water sensitive chemicals 		are designed to be inert and will not react with the reagent. Do not put water on the 		spill.

2. In the event of a spill alert personnel in the area that a spill has occurred. Do not 		attempt to handle a large spill of water sensitive chemicals. Turn off all ignition sources 		and vacate the laboratory immediately. Call 911 for assistance.

3. Remain on the scene, but at a safe distance, to receive and direct safety personnel 		when they arrive.

IX. Decontamination and Waste Disposal

A. 	Decontamination Procedures

1. Personnel:  Wash hands and arms with soap and water immediately after handling 		any chemicals.

2. Area:  Carefully clean work area after use.

3. Equipment:

B. Waste Disposal

All materials contaminated with water and air sensitive chemicals should be disposed of 		as hazardous waste. Alert the Chemical Hygiene Officer or the Division of 			Environmental Health and Safety if you generate wastes contaminated by water 			sensitive or pyrophoric chemicals. These wastes may pose a flammability risk and 		should not remain in the laboratory overnight.

X. 	Approvals

Some hazardous materials require special handling or prior approvals.  See Section 18 and 20 of the CHP.

XI. 	SOP Prepared by _______________________________________ Date _____________

Reviewed by ____________________________________________ Date ____________