SOP  8.	Standard Operating Procedure for Carcinogens

I.	General Statement of Coverage

A carcinogen commonly describes any agent that can initiate or speed the development of malignant or potentially malignant tumors, malignant neoplastic proliferation of cells, or cells that possess such material.  Common carcinogens found in laboratories include: Acrylonitrile, Benzene, Chromium (VI) and its salts, and Formaldehyde.

II.	Hazard Assessment

A Job Hazard Assessment should be performed for work involving carcinogenic materials and should address the issues of proper use and handling, chemical toxicity, storage, disposal, and required PPE.  See Section 21 and Form 4 of Section 25 of the Chemical Hygiene Plan.

III.	Resources

- Available Training

Chemistry 685

EHS/Chemistry Lab Safety Course

- Text and Literature References

Department of Chemistry Safety Handbook

“Degradation of Chemical Carcinogens” by Sansone and Slein, Nostrand, and Reinhold.

- CHP Appendix III (Section 23.3) Chemical Information Tables

Table 10.   Carcinogens Table

IV.	Chemical Storage

A.	Special Storage

Carcinogens should be handled in a designated area. Store carcinogens according to the hazard classification.

B.	Gas Cylinders

Gas cylinders must be secured while in use or in storage (empty or full).  They should be stored with the valve cap secured.  Refer to SOP #6-Compressed Gases.

V.	Personal Protective and Emergency Equipment

A. 	Eye and Face Protection

Refer to the Eye Protection Policy, Appendix IIB (Section 23.2).  At a minimum, safety glasses with permanently attached top and side shields must be worn in the laboratory.  These glasses, however, do NOT protect against splash hazards.  When performing a hazardous activity, a face shield must be worn in addition to the safety glasses OR switch to chemical splash goggles (with shielded ventilation ports).  Face shields are available from the Safety Office (free of charge).

B.	Gloves

Appropriate gloves should be worn when handling hazardous materials. The selection of glove materials should be made from Appendix II, Part A (Section 23.2) of this document.  If this chart is insufficient, please see the Safety Coordinator/CHO.

C.	Protective Clothing

Lab coats, closed toed shoes and long sleeved clothing should be worn when handling hazardous materials. Additional protective clothing, such as aprons or full-length arm protection, should be worn if the possibility of skin contact is likely.

D.	Hearing Protection

The use of hearing protection requires monitoring and training.  See the Safety Coordinator/CHO for details.

E.	Respirators

The use of respirators requires medical certification, fit testing, and training. See the Safety Coordinator/CHO for details.

F.	Eye Wash

Where the eyes or body of any person may be exposed to hazardous materials suitable facilities for quick drenching or flushing of the eyes and body shall be provided within, or near, the work area for immediate emergency use. Bottle type eyewash stations are not acceptable.

G. 	Safety Showers

A safety shower should be available and functioning as specified by ANSI Z358.1.

H.	Fire Extinguishers

All laboratories must contain at least one Carbon Dioxide (Type B-C) or Dry Chemical (Type A-B-C) fire extinguisher.  Additional fire extinguishers are located near exits and/or stairwells in each building.  Special Class D fire extinguishers (for certain metal fires) are available from the Safety Office.

VI.	Controls

A.	Designated Areas

- The acrylic laboratory door sign must be updated to include the type and approximate amount of carcinogens in use or storage.

- All locations within the laboratory (or the laboratory door itself) where carcinogens are handled should have posted with designated area caution signs. This includes all fume hoods and bench tops where the carcinogens are handled. Where feasible, carcinogens should be manipulated over plastic-backed disposable paper work surfaces. These disposable work surfaces minimize work area contamination and simplify clean up.  See Section 18 of the CHP.

- Training must be provided by the laboratory supervisor on the proper handling and storage techniques, waste disposal, and spill response involving each carcinogen used. This training must be documented.

B.	Chemical Fume Hoods

- Manipulation of carcinogens should be carried out in a fume hood. If the use of a fume hood proves impractical refer to the section on special ventilation.

- All areas where carcinogens are stored or manipulated must be labeled as a designated area.

C.	Glove Boxes

Certain carcinogens should be handled in a glove box rather than a fume hood.  Consult the Division of Environmental Health and Safety or the Laboratory Supervisor.  Refer to SOP 14 on the use of Dry Boxes.

D.	Safety Shielding

Safety shielding is required any time there is a risk of explosion, splash hazard or a highly exothermic reaction.  All manipulations of reactive chemicals which pose this risk should occur in a fume hood with the sash in the lowest feasible position. Portable shields, which provide protection to all laboratory occupants, are acceptable.

E.	Special Ventilation

- Manipulation of carcinogens outside of a fume hood may require special ventilation controls in order to minimize exposure to the material. Fume hoods provide the best protection against exposure to carcinogens in the laboratory and are the preferred ventilation control device. When possible, handle carcinogens in a fume hood. If the use of a fume hood proves impractical, attempt to work in a glove box or on an isolated area on the bench top.

- If available, consider using a Biological Safety Cabinet. The biological safety cabinet is designed to remove particulates (the carcinogen) before the air is discharged into the environment. Carcinogens that are volatile must not be used in a biological safety cabinet unless the cabinet is vented to the outdoors.

- If your research does not permit the handling of carcinogens in a fume hood, biological safety cabinet, or glove box, contact the Division of Environmental Health and Safety.

- All areas where carcinogens are manipulated must be labeled as a designated area.

F.	Vacuum Protection

- Evacuated glassware can implode and eject flying glass, and splattered chemicals. Vacuum work involving hazardous materials must be conducted in a fume hood, glove box or isolated in an acceptable manner.

- Mechanical vacuum pumps and the “House Vacuum System” must be protected using cold traps and, where appropriate, filtered to prevent particulate release. See the article on cold traps in the Department Safety Handbook under “Compressed Gases.”  The exhaust for the pumps should be vented into an exhaust hood.

G.	Signs and Labels

- Doorways: All OSHA Select Carcinogens, Reproductive Toxins, Highly Toxic materials, and NFPA Level 4 Flammable Liquids (Section 23.3, Tables 10-15) must be indicated on the acrylic door sign.

- Containers:  All hazardous materials must be clearly labeled with the correct chemical name.

H. 	Utilities

In Evans and Celeste Labs, utility shut-off valves are located in pipe chases just outside of the laboratories.  In Newman/Wolfrom, the valves are located above the ceiling in the hallways.  Look for the ceiling tiles with the green dots.

I.	Fire Protection

Older buildings, such as Evans and Johnston Labs, do not have sprinkler suppression systems.  This could be a consideration for storing or using large quantities of hazardous materials.

VII.	Specific Procedures

Refer to the MSDS or other sources of information to become familiar with the properties of the particular substances including: chemical and physical properties, health hazard information, symptoms of over-exposure, etc.

VIII.	Emergency Procedures

A.	Notification

Refer to the “Emergency Response” section of the Department Safety Handbook for generic emergency response procedures.  Specific emergency procedures should be developed for each group or laboratory.   The procedures should address as a minimum the following:

- Who to contact: (University police at 292-2121 or 292-2525, and Division of Environmental Health and Safety at 292-1284 during normal working hours, and the Principal Investigator of the laboratory including evening phone number).

- The location of all safety equipment (showers, spill equipment, eye wash, fire extinguishers, etc.).

- The location and quantity of all carcinogens in the laboratory.

- The method used to alert personnel in nearby areas of potential hazards.

- Special first aid treatment required by the type of chemicals handled in the laboratory

B.	Spill Response

- Anticipate spills by having the appropriate clean up equipment on hand. The appropriate clean up supplies can be determined by consulting the material safety data sheet.  This should occur prior to the use of any hazardous chemicals. Spill control materials for chemicals are designed to be inert and will not react with the reagent.

- In the event of a spill alert personnel in the area that a spill has occurred. Do not attempt to handle a large spill of carcinogenic materials.  Call the Safety Office for assistance.

- Remain on the scene, but at a safe distance, to receive and direct safety personnel when they arrive.

IX.	Decontamination and Waste Disposal

A.	Decontamination Procedures

- Personnel: Wash hands and arms with soap and water immediately after handling any chemicals.

- Area: Carefully clean work area after use.

- Equipment:

B.	Waste Disposal

All materials contaminated with carcinogenic chemicals should be disposed of as hazardous waste.  See the Department Safety Handbook for more information.

X.	 Approvals

Some hazardous materials require special handling or prior approvals.  See Sections 18 and 20 of the CHP.

XI.	SOP Prepared by _______________________________________ Date _____________

Reviewed by___________________________________________ Date _____________